## Slide 1: Team 9 Presentation
By Val Hahn, Derek Vogel, and Ja’lon Clark

## Slide 2: Overview
Processor Size and Composition
Components
Utilities
Testing Process
Demonstration

## Slide 3: Processor Size
16-bit processor
  Register files are limited to 16-bits
24-bit instruction size
  Contains Opcode, Cond, S, Source, Destination, Immediate, and T
  Works for D-type, S-type, J-type

## Slide 4: 5 Stages of the Processor
Fetch
Decode
Computer
Memory
Write

## Slide 5: Components
ALU
  Handles arithmetic of selected operations
  Can operate ADD, SUB, AND, OR, and XOR

## Slide 6: Components
Control Unit
  Takes the instructions and sends the op-code to the ALU
  Controls the path of processor and stages
  Sets the condition flags
PS Register
  Holds temporary conditional flags AFTER ALU operation
  Won’t update unless told so

## Slide 7: Components
Memory Interface
  Stores and retrieves values in main memory
  Accessed only by load and store instructions

## Slide 8: Components
Instruction Address Generator
  Program Counter
  Helps determine execution of instructions
  Contains Adder
    Assists with offsets and jumps

## Slide 9: Components
Instruction Register
  Directly stores instructions

## Slide 10: Components
IO Interface
  Where IO devices are stored and loaded from
  IO components include switches, push buttons, LEDs, and 7-segment display

## Slide 11: Instructions
D-Type Instructions
S-Type Instructions
J-Type Instructions

## Slide 12: D-Type Instructions
Add & Sub
  Done in the ALU
  Result value saved to register file
  Sub inverts the number before computation to subtract
And, Or, Xor
    Computes in the ALU to their specific logic gate
Load, Store & Compare
  Deals with memory interface

## Slide 13: S-Type Instructions
Inc & Dec
  Adds/Subtract immediate value of 1
Jr (Jump replace)
  Sets PC to destination register
Clr
  Clears all bits of destination register to 0

## Slide 14: J-Type Instructions
J
  Jumps to relative address
  Does not return anything
JL
  Same as J, but returns address in RA

## Slide 15: Speed
Base clock speed of 2000 ps per cycle
  Works perfectly
Doubling speed to 1000 ps per cycle crashes

## Slide 16: Testing
First tested Add, Sub, And, Or, and Xor
Load, Store, Branch, and were tested together
  Used that to test IO components
  Tested green LEDs, red LEDs, pushbuttons, switches, and drum kit.
    Successfully works

## Slide 17: LED Demonstration
vsim Team9_FinalProject view wave add wave Clock add wave RA add wave RB add wave RZ add wave RY add wave IR add wave BugAddress add wave BugDOut
add wave Bugmem_writeIO add wave Bugmem_writeMAIN add wave ZBug add wave LEDG force Clock 1 0, 0 1000 -repeat 2000 force NKEY 0001 0 run 400000

## Slide 18: Demonstration

## Slide 19: LED Demonstration
vsim Team9_FinalProject view wave add wave Clock add wave RA add wave RB add wave RZ add wave RY add wave IR add wave BugAddress add wave BugDOut
add wave Bugmem_writeIO add wave Bugmem_writeMAIN add wave ZBug add wave LEDG force Clock 1 0, 0 1000 -repeat 2000 force NKEY 0111 0 run 400000

## Slide 20: Demonstration